## Slide 1: FUTABA Communication Plan

## Slide 2: CW Beacon Format
Call Sign |  |  |  |  | 
J | G | 6 | Y | B | W
Satellite Name |  |  |  |  | 
F | U | T | A | B | A
House Keeping Data |  |  |  |  |  |  |  |  |  |  |  | 
Voltage of Battery |  | Temperature of Battery |  | Temperature of Communicator |  | Detection of Expanding Antenna | Success or Failure of Uplink | The number of reset | ADCS Control | Camera | Sensing Occurring Whisker | UV Sensor
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 13 | 14
4 | 4 | 4 | 4 | 4 | 4 | 1 | 1 | 2 | 2 | 2 | 2 | 6

## Slide 3
Call Number | Data |  | 
1 | Voltage of Battery | 4bit | 1byte
2 |  | 4bit | 
3 | Temperature of battery | 4bit | 1byte
4 |  | 4bit | 
5 | Temperature of Communicator | 4bit | 1byte
6 |  | 4bit | 
7 | Detection of Expanding Antenna | 1bit | 1byte
8 | Success or Failure of Uplink | 1bit | 
9 | The number of reset | 2bit | 
10 | ADCS control | 2bit | 
11 | Reserving Camera | 2bit | 
12 | Sensing Occurring of Whisker | 2bit | 1byte
13 | UV sensor | 6bit | 

## Slide 4
 | Subsystems | Contents | Details
1 | OBC | Reset Forcibly | Reset Forcibly All Microcomputer of OBC
2 |  |  | Rest Forcibly of ADCS
3 |  |  | Reset Forcibly of MISSION
4 |  | Latest Log | Requires Latest Log of OBC
5 |  | Selection Log | Requires Selection Log of OBC
6 |  | Kill Switch | Kill Switch turns ON
7 | Control Attitude | Taking Photo(Low Image Quality) | 
8 |  | Taking Photo(High Image Quality) | 
9 |  | Reset Camera | 
10 |  | Starting Stabilization | 
11 |  | Starting Three-axis | 
12 |  | Updating TLE | 
13 |  | Setting Stabilization | 
14 |  | Setting Three-axis | 
15 |  | Data Downlink(Sensor) | 
16 |  | Data Downlink(Camera) | 
17 |  | Getting Photo Information | 
18 |  | Next Unit | 
19 | Whisker | Taking Photo | 
20 |  | Reset Camera | 
21 |  | Data Downlink(Sensor) | 
22 |  | Getting Photo Information | 
23 |  | Next Unit | 
CF Command Format